## Slide 1: On-Device Binary Classification with Federated Learning using the STM32
Yingshuo Xi, Ali Jahangiri
Department of Electrical and Information Technology,
Lund University, Sweden.
This research has been partially supported by the Wallenberg AI, Autonomous Systems and Software Program (WASP), the Swedish Research Council (VR), the ELLIIT Strategic Research Environment, European Union, and an unrestricted gift from Google.

## Slide 2: Data Collection
On-device Training
Federated Learning
Data Collection
CONTENTS

## Slide 3: Dataset - acoustic dataset of brushless DC motors
Healthy
Dataset
(Data in Brief *)
Bearing
Propeller
Healthy
(class 0)
Defect
(class 1)
7
6
8
8
6
8
Train set
Validation set
Test set
Not used
* Prieto Estacio, R. S., Bravo Montenegro, D. A., & Rengifo Rodas, C. F. (2023). Dataset of audio signals from brushless DC motors for predictive maintenance.
Data in Brief, 50, 109569. https://doi.org/10.1016/j.dib.2023.109569

## Slide 4: Fourier Transform
To capture enough cycles (5) of the frequency (1000 Hz) based on the sampling rate (16000 Hz),
the minimal data points per sample: 80.

## Slide 5: Dataset - Overview
Label | Train | Validation | Test
0 | 14425 (46.80%) | 8236 (50.00%) | 8186 (49.94%)
1 | 16400 (53.20%) | 8236 (50.00%) | 8206 (50.06%)
total | 30825 | 16472 | 16392
Samples Per Set

## Slide 6: On-device Training
Data Collection
Federated Learning
CONTENTS
On-device Training

## Slide 7: UART Communication

## Slide 8: UART Protocal
1 bytes
CODE | Meaning
0x01 | Request_train
0x02 | Data
0x03 | Ack
0x04 | Finish
0x05 | End
0x06 | Result_train
0x07 | Request_val
0x08 | Result_val
0x09 | Request_test
0x0A | Result_test
start of frame
type
sequence
length
DATA
crc
2 bytes
2 bytes
length bytes
2 bytes
2 bytes
label
Data1(float)
data2
1 bytes
4 bytes

## Slide 9: Process and Flash
[Load] (Train + Val [Save?]) + …… + (Train + Val [Save?]) + Test
0x08000000
0x08078000
480K
Store
Program code
32K
Store
weights
FLASH
Start Code
Version
Length
crc
Accuracy
Data
NVM

## Slide 10: Model – Binary Forward-Forward
DATA
DATA
Correct Label
DATA
Wrong Label
FF Model
positive
negative
DATA
(label = 1)
DATA
(label = 0)
FF Model
positive
negative
Classical FF Model
Binary FF Model

## Slide 11: Results
Test acc: 0.8193
Test acc: 0.7731

## Slide 12: Results
Model | Accuracy | F1 score | AUC | Flash (Static) | RAM (Static) | RAM (Fixed) | RAM (Train)
BP | 0.82 | 0.80 | 0.91 | 38.8KB | 50.8KB | 15.9KB | 0.5KB
FF | 0.77 | 0.74 | 0.88 | 40.7KB | 52.4KB | 17.5KB | 0.8KB

## Slide 13: Federated Learning
Data Collection
Federated Learning
CONTENTS
On-device Training

## Slide 14: Federated Averaging
Implementation of FedAvg with two weights
Calculated on STM32 server module
After 2 epochs (i.e. 1 round), the weights are averaged and sent back to each board. For a total of 6 rounds

## Slide 15: Dataset – FL Split
Board | Train | Validation | Test
COM16 | 250 (55.55%) | 100 (22.22%) | 100 (22.22%)
COM21 | 250 (55.55%) | 100 (22.22%) | 100 (22.22%)
total | 500 | 200 | 100
Samples Per Device
Shared global test set

## Slide 16: BP Results - Epochs

## Slide 17: BP Results - Rounds

## Slide 18: FF Results - Epochs

## Slide 19: FF Results - Rounds

## Slide 20: Results
On-device training
Model | Accuracy | F1 score | AUC
BP | 0.82 | 0.80 | 0.91
FF | 0.77 | 0.74 | 0.88
Model | Accuracy | F1 score | AUC
BP | 0.72 | 0.64 | 0.83
FF | 0.54 | 0.32 | 0.36
Federated learning*
* Subset of whole dataset used for federated learning due to time limits

## Slide 21: Conclusion
On-device learning on the STM32 is possible, although slow (>1 day training)
A “simple” downsampling process can be used in lieu of FFT-based feature extraction
After 12 epochs, we can get 82% (BP) and 77% (FF) accuracy
After 6 rounds of 2 epochs, we can get accuracy of 72% (BP) and 54% (FF) via federated learning.
Setting up BLE on the STM32 remains a challenge, instead, weights are sent via UART
Increasing dataset should improve FF federated learning metrics

## Slide 22: Questions?
Thank you!